## Slide 1
Air Traffic Separation and
Collision Avoidance
Deconfliction &
Separation Management

## Slide 2
Ciconia deals with Deconfliction & Safe Separation
for “low & slow” since 2011 with the C&CAS:
“Control & Collision Avoidance System”
Safe separation for the UTM

## Slide 3
New standards & terminology required:
Maximum density of air traffic in a given volume
Examples:
Max speed between buildings: horizontal, vertical
Speed control
‘Street roof’ altitude
Minimum DbP (Distance between Platforms)
Minimum TtC (Time to Collision) between platforms
Safe separation for the UTM -

## Slide 4
‘Street Roof’ Altitude:
30m
90m
Roof top?
Roof top?
Only vertical speed below street roof?
Stop before climbing over street roof?
New standards & terminology required:
Setting ‘street roof’:

## Slide 5
Set by regulator
Enforced by:
C&CAS – decentralized density control
‘Density limit’
Strategic level while allocating air space to users
New standards & terminology required:
Too crowded!
(Min. range limit maintained)
- Maximum platforms in a given air volume:

## Slide 6
Minimum DbP (Distance between Platforms)
New standards & terminology required:
Minimum TtC (Time to Collision) between platforms
Separation between platforms:
Drone 1
area of operation
Drone 2
area of operation
Min distance
450m
Drone 1
max speed = 15m/s
TtC = 15sec.
Drone 2
max speed = 15m/s
450m
(15m/s + 15m/s)
= 15sec.

## Slide 7
Test case 1:
4
Unused air space!!!
3
2
5 drones operating in 5 areas
Min DbP (Distance between Platforms) > 450m
Min TtC (time to Collision) >= 15 sec.
Min DbP
450m
1
5

## Slide 8
Test case 2:
4
2
3
120m
5
TtC (Time to Collision) = 4sec.!
20m/(15m/s+ 15m/s)= 4sec
Smaller unused air space
but
5 drones operating in 5 areas
Min DbP (Distance between Platforms) > 120m
Min TtC (time to Collision) >= 15 sec.
1
To maintain TtC>= 15sec.,
Drones 2 & 4 must slow to 4m/sec [120m/(4m/s+4m/s)=15sec]

## Slide 9
Test case 2:
4
2
1
3
120m
5
450m,
Slow
Who will slow the drones in real time?
C&CAS – decentralized density control
Minimum unused air space
And
TtC limit (15 sec.) is kept
5 drones operating in 5 areas
Min DbP (Distance between Platforms) > 120m
Min TtC (time to Collision) >= 15 sec.

## Slide 10
Monitors constantly at the vehicle level:
Safe separation for the UTM –
new standards & terminology required:
Informs operators of potential separation violation
Ciconia decentralized C&CAS:
Displays steering commands to pilots; onboard & remote
Takes control over autopilot to avoid separation violation
TtC (Time to Collision)
DbP (Distance between Platforms)
Traffic density
RoC (Rate of Closure)

## Slide 11
A V2V network (remote ID?)
Enforcement of separation limits
ADS-B In data
Ciconia’s decentralized C&CAS (Control & Collision Avoidance)
Flight cues to human pilots
Steering commands to autopilots
C&CAS introduces:
C&CAS Flight Cues
Drone’s C&CAS unit
Coordinates
Coordinates
Coordinates
ADS B out
ADS B out
ADS B out
Drone’s C&CAS unit
Helicopter C&CAS unit
Remote pilot C&CAS unit
ADS B out

## Slide 12
As sophisticated as the ATM may be, there will be midair traffic conflicts!
Conclusion
New terminology & limits required (‘street roof’, ‘traffic density’, etc.)
Decentralized monitoring & enforcement is the only way to ensure safety of flight and efficient use of airspace

## Slide 13
Conclusion (Cont.)
Ciconia’s C&CAS has been proven in flight tests
Decentralized C&CAS will allow more traffic while keeping highest
safety standards
Thank you!